## Slide 1: NS-2 Tutorial
Sung Park
Network and Embedded Systems Lab (NESL)
Electrical Engineering, UCLA

## Slide 2: About This Tutorial
Based on ns Tutorial (IX, XI) and ns manual (Chapter 14)
  Can be obtained from http://www.isi.edu/nsnam/ns
  Latest ns release is ns2.1b9
Will not discuss installation process
  Installation in linux machine is straightforward
  Support for SunOS and Windows(??)

## Slide 3: ns-2 overview
Collection of various protocols at multiple layers
  TCP(reno, tahoe, vegas, sack)
  MAC(802.11, 802.3, TDMA)
  Ad-hoc Routing (DSDV, DSR, AODV, TORA)
  Sensor Network (diffusion, gaf)
  Multicast protocols, Satellite protocols, and many others
Codes are contributed from multiple research communities
  Good: Large set of simulation modules
  Bad: Level of support and documentation varies
The source code and documentation is currently maintained by VINT project at ISI

## Slide 4: Introduction
ns-2 is an discrete event driven simulation
  Physical activities are translated to events
  Events are queued and processed in the order of their scheduled occurrences
  Time progresses as the events are processed
1
2
Time: 1.5 sec
Time: 1.7 sec
Time: 1.8 sec
Time: 2.0 sec

## Slide 5: Event Driven Simulation
TX Pkt Event @ 1.5sec
Node 1 Module
Node 2 Module
TX Pkt Event @ 1.5sec
RX Pkt Event @ 1.7sec
RX Pkt Event @ 1.7sec
TX Ack Event @ 1.8sec
TX Ack Event @ 1.8sec
RX Ack Event @ 2.0sec
RX Ack Event @ 2.0sec
Event Queue
Simulation Finished!

## Slide 6: ns-2 Environment
Simulation Scenario
Tcl Script
C++ Implementation
1
2
set ns_ [new Simulator]
set node_(0) [$ns_ node]
set node_(1) [$ns_ node]
class MobileNode : public Node
{
friend class PositionHandler;
public:
MobileNode();
•
•
}

## Slide 7: Why two languages? (Tcl & C++)
C++: Detailed protocol simulations require systems programming language
  byte manipulation, packet processing, algorithm implementation
  Run time speed is important
  Turn around time (run simulation, find bug, fix bug, recompile, re-run) is slower
Tcl: Simulation of slightly varying parameters or configurations
  quickly exploring a number of scenarios
  iteration time (change the model and re-run) is more important

## Slide 8: Tcl or C++?
Tcl
  Simple Configuration, Setup, Scenario
  If it’s something that can be done without modifying existing Tcl module.
C++
  Anything that requires processing each packet
  Needs to change behavior of existing module

## Slide 9: Wireless Simulation in ns-2
Contributed from CMU’s Monarch project (Wireless extension to ns-2)
Various modules were added to ns-2 to simulate node mobility and wireless networking
  Mobile Node
  Ad-hoc Routing(DSR, DSDV, TORA, AODV)
  MAC802.11
  Radio Propagation Model
  Channel

## Slide 10: Mobile Node Modules
Agent
  Responsible for packet generations and receptions
  Can think of it as an Application layer
  CBR(Constant Bit Rate), TCP, Sink, FTP, etc.
RTagent(DSDV, TORA, AODV) or DSR
  Ad-hoc network routing protocols
  Configure multi hop routes for packets
LL (Link Layer)
  Runs data link protocols
  Fragmentation and reassembly of packet
  Runs Address Resolution Protocol(ARP) to resolve IP address to MAC address conversions

## Slide 11: Mobile Node Modules (Continued)
IFq (Interface Queue)
  PriQueue is implemented to give priority to routing protocol packets
  Supports filter to remove packets destined to specific address
Mac Layer
  IEEE 802.11 protocol is implemented
  Uses RTS/CTS/DATA/ACK pattern for all unicast pkts and DATA for broadcast pkts

## Slide 12: Mobile Node Modules (Continued)
NetIF (Network Interfaces)
  Hardware interface used by mobilenode to access the channel
  Simulates signal integrity, collision, tx error
  Mark each transmitted packet with transmission power, wavelength etc.
Radio Propagation Model
  Uses Friss-space attenuation(1/r2) at near distance and Two ray ground (1/r4) at far distance
  Decides whether the packet can be received by the mobilenode with given distance, transmit power and wavelength
  Implements Omni Directional Antenna module which has unity gain for all direction

## Slide 13: Wireless Simulation in ns-2 (Mobile Node Diagram - DSDV)

## Slide 14: Wireless Simulation in ns-2 (Mobile Node Diagram - DSR)

## Slide 15: Running a simulation-Scenario
500m
500m
node_(0)
TCP
node_(1)
TCPsink
node_(0)
TCP
node_(1)
TCPsink
node_(0)
TCP
node_(1)
TCPsink

## Slide 16: Setting Up Variables
#======================================================================
# Define options
#======================================================================
set val(chan) Channel/WirelessChannel ;# channel type
set val(prop) Propagation/TwoRayGround ;# radio-propagation model
set val(ant) Antenna/OmniAntenna ;# Antenna type
set val(ll) LL ;# Link layer type
set val(ifq) Queue/DropTail/PriQueue ;# Interface queue type
set val(ifqlen) 50 ;# max packet in ifq
set val(netif) Phy/WirelessPhy ;# network interface type
set val(mac) Mac/802_11 ;# MAC type
set val(rp) DSDV ;# ad-hoc routing protocol
set val(nn) 2 ;# number of mobilenodes

## Slide 17: Setting Up Variables
Instantiate simulator object
set topo [new Topography]
$topo load_flatgrid 500 500
set ns_ [new Simulator]
set tracefd [open simple.tr w]
$ns_ trace-all $tracefd
create-god $val(nn)
Setup Trace File
Create Topography
Create Object God

## Slide 18: Configuring Mobilenode
# Configure nodes
$ns_ node-config -adhocRouting $val(rp) \
-llType $val(ll) \
-macType $val(mac) \
-ifqType $val(ifq) \
-ifqLen $val(ifqlen) \
-antType $val(ant) \
-propType $val(prop) \
-phyType $val(netif) \
-topoInstance $topo \
-channelType $val(chan) \
-agentTrace ON \
-routerTrace ON \
-macTrace OFF \
-movementTrace OFF
for {set i 0} {$i < $val(nn) } {incr i} {
set node_($i) [$ns_ node ]
$node_($i) random-motion 0 ;# disable random motion
}

## Slide 19: Configuring Movement
Configure Initial Position
# Node_(1) starts to move towards node_(0)
$ns_ at 50.0 "$node_(1) setdest 25.0 20.0 15.0"
$ns_ at 10.0 "$node_(0) setdest 20.0 18.0 1.0"
# Node_(1) then starts to move away from node_(0)
$ns_ at 100.0 "$node_(1) setdest 490.0 480.0 15.0"
$node_(0) set X_ 5.0
$node_(0) set Y_ 2.0
$node_(0) set Z_ 0.0
$node_(1) set X_ 390.0
$node_(1) set Y_ 385.0
$node_(1) set Z_ 0.0
Create Movement

## Slide 20: Setup traffic flow
set tcp [new Agent/TCP]
$tcp set class_ 2 set sink [new Agent/TCPSink]
$ns_ attach-agent $node_(0)
$tcp $ns_ attach-agent $node_(1)
$sink $ns_ connect $tcp
$sink set ftp [new Application/FTP]
$ftp attach-agent $tcp $ns_ at 10.0 "$ftp start"
node_(0)
FTP
TCP
node_(1)
Sink

## Slide 21: Set Stop Time and Start Simulation
Set Simulation Stop Time
puts "Starting Simulation..."
$ns_ run
for {set i 0} {$i < $val(nn) } {incr i} {
$ns_ at 150.0 "$node_($i) reset";
}
$ns_ at 150.0001 "stop"
$ns_ at 150.0002 "puts \"NS EXITING...\" ;
$ns_ halt" proc stop {} { global ns_ tracefd close $tracefd }
Finally, Start The Simulation

## Slide 22: Running the Script
The file “simple-wireless.tcl” is under <NSRoot>/ns-allinone2.1b9/ns-tutorial/examples/simple-wireless.tcl
cd into the directory and type “ns simple-wireless.tcl” to run the simulation
The simulation will generate a trace file named “simple.tr”

## Slide 23: Trace File
r 100.381997477 _1_ AGT --- 82 tcp 1060 [13a 1 0 800] ------- [0:0 1:0 32 1] [32 0] 1 0
r:receive event, 100.381997477:time stamps,
_1_:node 1, AGT:trace generated by agent, 82:event(pkt) id, tcp: tcp packet,
1060:packet size,
13a(hex):expected duration of pkt transmission (not working), 1:sender mac id, 0:transmitter mac id,
800:pkt type IP (806 for ARP), 0:0: sender address:port#
1:0: receiver address:port#, 32: TTL
1: next hop address, [32 0]: TCP sequence #, ack #

## Slide 24: SensorViz:GUI based Scenario Generation Tool
http://nesl.ee.ucla.edu/projects/sensorsim/

## Slide 25: Using SensorViz output
SensorViz output may look like the following
source “filename”
# number of nodes = 2
# dimension x = 20000
# dimension y = 20000
# transmission range = 3000.0
# beacon = 4
$node_(0) set X_ 12415.458937198067
$node_(0) set Y_ 11612.90322580645
$node_(0) set Z_ 0.0
$node_(1) set X_ 7874.396135265701
$node_(1) set Y_ 8585.607940446649
$node_(1) set Z_ 0.0
Simply include the file by using “Source” command in your main tcl scpript

## Slide 26: Tips on using ns-2
Requires a good knowledge of C++
Good idea to start with the existing tcl script
Make sure to configure the position of all the nodes that you create
If you want to find a filename with a specific term, use “find” command
  find . –name “*tcp*” –print
ns has support for basestation setting wireless network. gaf and diffusion codes are included
If it’s possible, use the existing trace file for your analysis. Otherwise, you can use cout or (printf) to output your results